## Slide 1: Automated recording system to monitor grasshopper abundance in natural environments

## Slide 2: Introduction: long-term goal
Monitoring data to study change on biodiversity.
Embedded recording system
  Goal : do an algorithm that recognise from sound orthoptera in Swiss landscape
Notes: - Manual samplig: take time, time is money… So have an embedded system that records the species will be interesting
- Explain what is manual sampling : have to catch the insects by hand, then an entomologist have to recognize it by hearing…

## Slide 3: Introduction: this project
First implementation based on a published paper (Ganchev, 2007)
Two methods to extract the features :
  Variable length frame size
  Fixed frame size
Features used :
  Main frequency
  23 first LFCC
  Time duration (in case of variable length)
Classifier : GMM

## Slide 4: Variable VS Fixed frame size
Variable length frame
  Activity detector based on energy and threshold
Fixed frame size
  Cut the signal every e.g.100 m
  Threshold to select most significant frames
Notes: Two different ways to extract the frame that contains the features

## Slide 5: Data
Test files recorded on the field, 03.08.15
  Recognized “by hearing” (C. Roesti)
  Our study focus only on the 7 species recorded that day
Database of songs from “Die Stimmen der Heuschrecken”, Christian Roesti
  Data was processed to keep files containing only calling songs recorded with standard recorder
Finally : we have 3 to 10 files per species
Notes: We selected 7 species, recorded on the field

## Slide 6: Classification
Classifier
Record to identify
Features
Extraction
Search for similarity
Decision
Training data
Features
Extraction
GMM Species Models
From database
From database
or field recordings
Notes: - First we have to train a model
- Then we can classify a new signal, coming from the field for example

## Slide 7: Training / Testing methods
Data must be separate into a training and a testing set
There is different ways to chose the testing set :
  All versus all
  Cross-validation
  One versus all
It leads to different results depending on the method chosen

## Slide 8: All versus all
File N
File 2
File 4
File 1
File 3
…
File i
All the files are used to train, then each file is used to test
Training set
Testing set
i = 1 … N

## Slide 9: Cross validation (e.g. 5-fold)
All the features vector from all files are blend, then 4/5 is for training, 1/5 for testing
  Five different data-splits
  Ganchev 2007 uses 2-fold cross-validation (having only one file per individual)
Training set
Testing set
File N
File 2
File 4
File 1
File 3
…
Vector 3
Vector …
Vector 2
Vector 13
Vector 42
Vector 1205
Vector 1
Vector 21
grouped by species
grouped by file

## Slide 10: One versus all
File …
File 3
File 5
File 2
File 4
File 6
File 1
A file is retired from training set and tested after
  Done for each file
More representative of the real system
Training set
Testing set
Notes: We put aside one file and take the remaining to train
Real world condition

## Slide 11: Todor Ganchev’s paper
«Automatic acoustic identification of singing insects», Ganchev & Potamitis, 2007
Method
  Fixed frame size & variable length size
  Time duration, main frequency, 23 LFCC
  GMM & PNN classifier
Accuracy ~ 95% (warning !)
Database source: SINA, ISW, NAVIS
  307 species to detect
  One file per species
    ½ for training, ½ for testing
Notes: Our principal guideline is this paper…
SINA : Singing insects of north America
ISW : Insect sound world - Japan
NAVIS : Natural Audio and Video Documentation of Slovenia

## Slide 12: Previous Results : bad hope
Core of the naive Bayes classifier code
  ~ 75% of good classification
Core of the discriminant analysis code
  ~ 80-90% of good classification
  Cross validation method was used
  The same file was used to train and test, but not the same features vectors

## Slide 13: Results
 | All VS All | Cross Validation | One VS All
Fixed Frame | 94.44 % 97.22 % * | 95.55 % 96.11 % * | 36.11 % 44.44 % *
Variable Length |  | 94.6 % | 55.55 %
Using 13 field recording files : 30.7 %
Accuracy decreases drastically when we’re implementing the “one versus all”
  Lack of data, we would need at least 10 files per species!
* Using resampling to have the same features vector ratio among each species
Notes: Considering the confusion matrix, we see that the species which contain more files are easier to predict

## Slide 14: Conclusion
Results can be distorted depending on the choice of the test methodology
A large amount of files per individuals is preferred (~ 15)
  If we have 2 files for an individual, that mean one files would be used for training and one for testing…
  The differences between individuals within a species are not “averaged out” and removed
One versus all is the “real condition” method, which shows the generalization ability of our system
Notes: Distorted / Biased

## Slide 15: Future work
More clean, labelled data should be obtained
Study other methods
  Sound parametrization:
    Time & frequency parameters (e.g. OpenSmile)
    Filter banks or wavelets
  Classifier: PNN, HMM

## Slide 16: Thank you for your attention